## Slide 1: Computer Architecture & Assembly Language CSC-250
COURSE LECTURE
COMPUTER SCIENCE DEPARTMENT
SIBAU KANDHKOT CAMPUS

## Slide 2: History of computer
MECHANICAL
ELOCTRO MECHANICAL
ELECTRONIC

## Slide 3: ENIAC
Electronic Numerical Integrator And Computer
Decimal (not binary)
20 accumulators of 10 digits (ACCUMULATOR:
Programmed manually by switches
18,000 vacuum tubes
30 tons
15,000 square feet
140 kW power consumption
5,000 additions per second
An accumulator is a register for short-term, intermediate storage of arithmetic and logic data in a computer's CPU The term "accumulator" is rarely used in reference to contemporary CPUs, having been replaced around the turn of the millennium by the term "register." In a modern computers, any register can function as an accumulator
First Task was to check feasibility of hydrogen bomb through experiments
Used until 1955

## Slide 4: von Neumann/Turing
Stored Program concept
Main memory storing programs and data
ALU operating on binary data
Control unit interpreting instructions from memory and executing
Input and output equipment operated by control unit
Princeton Institute for Advanced Studies (IAS) computer
Completed 1952

## Slide 5: Structure of von Neumann machine

## Slide 6: John von Neumann and the IAS machine, 1952

## Slide 7: Word
IAS contains 1000 storage locations:
  Each called a word (40 Binary Digits)
    Store Data and Instructions

## Slide 8: IAS Memory Formats

## Slide 9: Registers

## Slide 10: IAS Operation
Operates by repetitively performing an instruction cycle
  Fetch
    Opcode of next instruction is loaded in IR
    Address portion is loaded in MAR
  Execute
    Interpretation of OPCODE
    Control signals are sent to ALU to execute

## Slide 11: IAS Instructions
21 Instructions

## Slide 12: Commercial Computers
UNIVAC I(Universal Automatic Computer):
  First Commercial computer
US Bureau of Census for the 1950 calculations
Late 1950s -UNIVAC II
  —Faster
  —More memory
Every organization makes backward compatible PCs:
  Clients always try to buy from the same vendor
    No Loss in purchase of software programs

## Slide 13: IBM (International Business Machines Corporation)
1953 -the 701
  IBM’s first stored program computer
Scientific calculations
1955 -the 702
  Business applications
Made IBM Dominant manufacturer

## Slide 14: Transistors
Replaced vacuum tubes
Smaller
Cheaper
Less heat dissipation
Solid State device
Made from Silicon (Sand)
Invented 1947 at Bell Labs

## Slide 15: Transistor Based Computers
Second generation machines
High Level Languages, System Software
NCR & RCA produced small transistor machines
IBM 7000
DEC - 1957
  Produced PDP-1

## Slide 16: THE IBM 7094

## Slide 17: Third Generation
Number of Transistors were growing in PCS:
  Lead to larger size:
    Affected Speed
    Development of Microelectronics

## Slide 18: Microelectronics
Literally - “small electronics”
A computer performs data processing, data control, I/O etc:
  Gates, memory cells are enough
    These can be manufactured on a semiconductor
    e.g. silicon wafer (SSI)

## Slide 19: WAFER

## Slide 20: IBM 360

## Slide 21: Characteristics of Family
Similar or Identical Instruction set:
  Almost same machine instructions
  Programs can run on any machine of family
Similar or Identical OS:
  Same OS
  Additional features
Going up:
  Increasing Speed
  Increasing I/O Ports
  Increasing Memory Size
  Increasing Cost

## Slide 22: DEC PDP-8
Same year(IBM system/360) –PDP-8 from Digital Equipment Corporation
Small enough to be placed on top of bench
No air-conditioned room required
Cheap enough (Not exact functionality like mainframe)
No central switch architecture (Fig.1.9) IBM
Introduced the concept of Omnibus( Bus structure for microcomputers)

## Slide 23: Generations of Computers
Vacuum tube -1946-1957
Transistor -1958-1964
Small scale integration -1965 on
Up to 100 devices on a chip
Medium scale integration -to 1971
100-3,000 devices on a chip
Large scale integration -1971-1977
3,000 -100,000 devices on a chip
Very large scale integration -1978 -1991
100,000 -100,000,000 devices on a chip
Ultra large scale integration –1991 -
Over 100,000,000 devices on a chip

## Slide 24: Moore’s Law
Increased density of components on chip
Gordon Moore –co-founder of Intel
Number of transistors on a chip will double every year
Since 1970’s development has slowed a little
Number of transistors doubles every 18 months
Cost of a chip has remained almost unchanged
Higher packing density means shorter electrical paths, giving higher performance
Smaller size gives increased flexibility
Reduced power and cooling requirements
Fewer interconnections increases reliability

## Slide 25: Rock’s Law
Arthur Rock, is a corollary to Moore’s law: “The cost of capital equipment to build semiconductor will double every four years”
Rock’s Law arises from the observations of a financier who has seen the price tag of new chip facilities escalate from about $12,000 in 1968 to $12 million in the late 1990s.
At this rate, by the year 2035, not only will the size of a memory element be smaller than an atom, but it would also require the entire wealth of the world to build a single chip!
So even if we continue to make chips smaller and faster, the ultimate question may be whether we can afford to build them

## Slide 26: 1st Generation Computers
  Used vacuum tubes for logic and storage (very little storage available)
  A vacuum-tube circuit storing 1 byte
  Programmed in machine language
  Often programmed by physical connection (hardwiring)
  Slow, unreliable, expensive
  The ENIAC – often thought of as the first programmable electronic computer – 1946
  17468 vacuum tubes, 1800 square feet, 30 tons

## Slide 27: 2nd Generation Computers
Transistors replaced vacuum tubes
Magnetic core memory introduced
  Changes in technology brought about cheaper and more reliable computers (vacuum tubes were very unreliable)
  Because these units were smaller, they were closer together providing a speedup over vacuum tubes
  Various programming languages introduced (assembly, high-level)
  Rudimentary OS developed
    The first supercomputer was introduced, CDC 6600 ($10 million)

## Slide 28: Second generation of computers Transistors
Replaced vacuum tubes
Smaller
Cheaper
Less heat dissipation
Solid State device
Made from Silicon (Sand)
Invented 1947 at Bell Labs by William Shockley et al.

## Slide 29: 3rd Generation Computers
ability to place circuits onto silicon chips
  Replaced both transistors and magnetic core memory
  Result was easily mass-produced components reducing the cost of computer manufacturing significantly
  Also increased speed and memory capacity
  Computer families introduced
  Minicomputers introduced
  More sophisticated programming languages and OS developed
    Popular computers included PDP-8, PDP-11, IBM 360 and Cray produced their first supercomputer, Cray-1
  Silicon chips now contained both logic (CPU) and memory
  Large-scale computer usage led to time-sharing OS

## Slide 30: 4th Generation Computers 1971-Present: Microprocessors
Miniaturization took over
  From (10-100 components per chip) to (10,000+)
Thousands of ICs were built onto a single silicon chip(VLSI), which allowed Intel, in 1971, to
  create the world’s first microprocessor, the 4004, which was a fully functional, 4-bit system that ran at 108KHz.
  Intel also introduced the RAM chip, accommodating 4Kb of memory on a single chip. This allowed computers of the 4th generation to become smaller and faster than their solid-state predecessors
  Computers also saw the development of GUIs, the mouse and handheld devices

## Slide 31: Microprocessors -Intel
1971 -4004
First microprocessor
All CPU components on a single chip
4 bit
Multiplication by repeated addition, no hardware multiplier!
Followed in 1972 by 8008
8 bit
Both designed for specific applications
1974 -8080
Intel’s first general purpose microprocessor

## Slide 32: Computer Level Hierarchy

## Slide 33: The Von Neumann Architecture
Named after John von Neumann, Princeton, he designed a computer architecture whereby data and instructions would be retrieved from memory,
operated on by an ALU, and moved back to memory (or I/O)
This architecture is the basis for most modern computers (only parallel processors and a few other unique architectures use a different model)

## Slide 34
Hardware consists of 3 units
  CPU (control unit, ALU, registers)
  Memory (stores programs and data)
  I/O System (including secondary storage)
Instructions in memory are executed sequentially

## Slide 35: Von Neumann Architectures
There is a single pathway used to move both data and instructions between memory, I/O and CPU
  the pathway is implemented as a bus
  the single pathway creates a bottleneck
    known as the von Neumann bottleneck
  A variation of this architecture is the Harvard architecture which separates data and instructions into two pathways
  Another variation, used in most computers, is the system bus version in which there are different buses between CPU and memory and memory and I/O

## Slide 36: Fetch-execute cycle
The von Neumann architecture operates on the fetch-execute cycle
  Fetch an instruction from memory as indicated by the Program Counter register
  Decode the instruction in the control unit
  Data operands needed for the instruction are fetched from memory
  Execute the instruction in the ALU storing the result in a register
  Move the result back to memory if needed

## Slide 37: The von Neumann Model
This is a general depiction of a von Neumann system:
These computers employ a fetch-decode-execute cycle to run programs as follows . . .

## Slide 38: The von Neumann Model
The control unit fetches the next instruction from memory using the program counter to determine where the instruction is located

## Slide 39: The von Neumann Model
The instruction is decoded into a language that the ALU can understand.

## Slide 40: The von Neumann Model
Any data operands required to execute the instruction are fetched from memory and placed into registers within the CPU.

## Slide 41: The von Neumann Model
The ALU executes the instruction and places results in registers or memory.