## Slide 1: Computer Components
A computer is a complex device containing many sub-systems. Each sub-system is a piece of computer hardware (or part of a piece of computer hardware.)
How these pieces interact is called the "Computer Architecture". The hard of a computer includes:
CPU - the ?brain? of the computer
Motherboard - The spine of the computer
Power Supply - the ?stomach? of the computer
BUS - "trucks" data around the computer
Clock - tells the CPU to start the next instruction
Network Card - the ?cell phone? of the computer
Monitor - the ?face? of the computer
Fans - computers can cook food, they are so hot. We must cool them down.

## Slide 2: Computer Components
virtually all contemporary computer designs are based on concepts developed by John von Neumann at the Institute for Advanced Studies, Princeton. Such a design is referred to as the von Neumann architecture and is based on three key concepts:
Data and instructions are stored in a single read–write memory.
The contents of this memory are addressable by location, without regard to the type of data contained there.
Execution occurs in a sequential fashion (unless explicitly modified) from oneinstruction to the next.

## Slide 3: Computer Components
Memory
Memory Layers
Registers (1 clock cycle)
Primary Cache: ~1 nano-second cache primary
Secondary Cache: 10 nano-seconds
fast RAM: 70 nanoseconds or less
fast disk: 10 milliseconds (10,000,000 nanoseconds)
CD/DVD: 160 milliseconds (160,000,000 nanoseconds)

## Slide 4: Computer Components
IO Devices
CPU
Memory
Graphics Card / Monitor
Keyboard
Disk Drive
Tape Backup
CD ROM

## Slide 5: Computer Components
  Originally computers used a Hardwired program
  The result of the process of connecting the various components in the desired configuration
  The computer must be rewired to run a different program
Contemporary computer designs are based on concepts developed by John von Neumann at the Institute for Advanced Studies, Princeton
Referred to as the von Neumann architecture it has three key concepts:
  Data and instructions are stored in a single read-write memory
  The contents of this memory are addressable by location, without regard to the type of data contained there
  Execution occurs in a sequential fashion (unless explicitly modified) from one instruction to the next
Notes: As discussed in Chapter 2, virtually all contemporary computer designs are based
on concepts developed by John von Neumann at the Institute for Advanced Studies,
Princeton. Such a design is referred to as the von Neumann architecture and is based
on three key concepts:
• Data and instructions are stored in a single read–write memory.
• The contents of this memory are addressable by location, without regard to
the type of data contained there.
• Execution occurs in a sequential fashion (unless explicitly modified) from one
instruction to the next.
The reasoning behind these concepts was discussed in Chapter 2 but is worth
summarizing here. There is a small set of basic logic components that can be
combined in various ways to store binary data and perform arithmetic and logical
operations on that data. If there is a particular computation to be performed, a
configuration of logic components designed specifically for that computation could
be constructed. We can think of the process of connecting the various components
in the desired configuration as a form of programming. The resulting “program” is
in the form of hardware and is termed a hardwired program.

## Slide 6: Function of Control Unit
A unique code for each operation
  Example: ADD, MOVE
Hardware Segment
Issues control signals
Accept codes

## Slide 7: Computer Components
PC = Program Counter
IR = Instruction Register
MAR = Memory Address Register
MBR = Memory Buffer Register
I/O AR = Input/Output Address Register
I/O BR = Input/Output Buffer Register
Computer
Central Processing Unit (CPU)
I/O Module
Buffers
Main Memory
Instruction
.
.
.
.
.
.
Instruction
Data
Data
.
.
.
0
1
2
.
.
.
PC
MAR
MBR
I/O AR
I/O BR
IR
Execution Unit
.
.
System
Bus

## Slide 8: Fetch Cycle
Program Counter (PC)
Holds address of next instruction to fetch
Processor
Fetch instruction from memory location pointed to by PC
Increment PC
Instruction Register (IR)
Load the instruction
Processor
Interprets instruction
Perform required actions

## Slide 9: Execute Cycle
Processor -Memory
Execution Cycle
Processor I/O
Data Processing
Control

## Slide 10: Hardware and Software Approaches
Notes: Now consider this alternative. Suppose we construct a general-purpose
configuration of arithmetic and logic functions. This set of hardware will perform
various functions on data depending on control signals applied to the hardware.
In the original case of customized hardware, the system accepts data and produces
results (Figure 3.1a). With general-purpose hardware, the system accepts data and
control signals and produces results. Thus, instead of rewiring the hardware for each
new program, the programmer merely needs to supply a new set of control signals.
How shall control signals be supplied? The answer is simple but subtle. The
entire program is actually a sequence of steps. At each step, some arithmetic or
logical operation is performed on some data. For each step, a new set of control
signals is needed. Let us provide a unique code for each possible set of control
signals, and let us add to the general-purpose hardware a segment that can accept a
code and generate control signals (Figure 3.1b).

## Slide 11: I/O Components
Software
A sequence of codes or instructions
Part of the hardware interprets each instruction and generates control signals
Provide a new sequence of codes for each new program instead of rewiring the hardware
Major components:
Means of reporting results
Output module
Contains basic components for accepting data and instructions and converting them into an internal form of signals usable by the system
Input module
I/O Components
Module of general-purpose arithmetic and logic functions
Instruction interpreter
CPU
Software
Notes: Programming is now much easier. Instead of rewiring the hardware for each
new program, all we need to do is provide a new sequence of codes. Each code
is, in effect, an instruction, and part of the hardware interprets each instruction
and generates control signals. To distinguish this new method of programming, a
sequence of codes or instructions is called software.
Figure 3.1b indicates two major components of the system: an instruction
interpreter and a module of general-purpose arithmetic and logic functions. These
two constitute the CPU. Several other components are needed to yield a functioning
computer. Data and instructions must be put into the system. For this we need some
sort of input module. This module contains basic components for accepting data
and instructions in some form and converting them into an internal form of signals
usable by the system. A means of reporting results is needed, and this is in the form
of an output module. Taken together, these are referred to as I/O components.

## Slide 12: MEMORY
Memory address register (MAR)
Specifies the address in memory for the next read or write
Memory buffer register (MBR)
Contains the data to be written into memory or receives the data read from memory
I/O address register (I/OAR)
Specifies a particular I/O device
I/O buffer register (I/OBR)
Used for the exchange of data between an I/O module and the CPU
MAR
MBR
Notes: One more component is needed. An input device will bring instructions and
data in sequentially. But a program is not invariably executed sequentially; it may
jump around (e.g., the IAS jump instruction). Similarly, operations on data may
require access to more than just one element at a time in a predetermined sequence.
Thus, there must be a place to store temporarily both instructions and data. That
module is called memory, or main memory, to distinguish it from external storage or
peripheral devices. Von Neumann pointed out that the same memory could be used
to store both instructions and data.
The CPU exchanges data with memory. For this purpose, it typically
makes use of two internal (to the CPU) registers: a memory address register (MAR),
which specifies the address in memory for the next read or write, and a memory
buffer register (MBR), which contains the data to be written into memory or receives
the data read from memory. Similarly, an I/O address register (I/OAR) specifies a
particular I/O device. An I/O buffer (I/OBR) register is used for the exchange of
data between an I/O module and the CPU.

## Slide 13: Fetch Cycle
At the beginning of each instruction cycle the processor fetches an instruction from memory
  The program counter (PC) holds the address of the instruction to be fetched next
  The processor increments the PC after each instruction fetch so that it will fetch the next instruction in sequence
The fetched instruction is loaded into the instruction register (IR)
  The processor interprets the instruction and performs the required action
Notes: At the beginning of each instruction cycle, the processor fetches an instruction
from memory. In a typical processor, a register called the program counter (PC)
holds the address of the instruction to be fetched next. Unless told otherwise, the
processor always increments the PC after each instruction fetch so that it will fetch
the next instruction in sequence (i.e., the instruction located at the next higher memory
address). So, for example, consider a computer in which each instruction occupies
one 16-bit word of memory. Assume that the program counter is set to memory
location 300, where the location address refers to a 16-bit word. The processor will
next fetch the instruction at location 300. On succeeding instruction cycles, it will
fetch instructions from locations 301, 302, 303, and so on. This sequence may be
altered, as explained presently.
The fetched instruction is loaded into a register in the processor known as
the instruction register (IR). The instruction contains bits that specify the action
the processor is to take. The processor interprets the instruction and performs the
required action.

## Slide 14
Notes: Figure 3.2 illustrates these top-level components and suggests the interactions
among them.
A memory module consists of a set of locations, defined by sequentially
numbered addresses. Each location contains a binary number that can be interpreted
as either an instruction or data. An I/O module transfers data from external devices
to CPU and memory, and vice versa. It contains internal buffers for temporarily
holding these data until they can be sent on.

## Slide 15
Fetch Cycle/Execute Cycle
We will expand and add details to these basic fetch and execute cycles throughout the lecture
Notes: The basic function performed by a computer is execution of a program, which consists
of a set of instructions stored in memory. The processor does the actual work by
executing instructions specified in the program. This section provides an overview of
the key elements of program execution. In its simplest form, instruction processing
consists of two steps: The processor reads (fetches ) instructions from memory one
at a time and executes each instruction. Program execution consists of repeating
the process of instruction fetch and instruction execution. The instruction execution
may involve several operations and depends on the nature of the instruction (see, for
example, the lower portion of Figure 2.4).
The processing required for a single instruction is called an instruction cycle.
Using the simplified two-step description given previously, the instruction cycle is
depicted in Figure 3.3. The two steps are referred to as the fetch cycle and the execute
cycle. Program execution halts only if the machine is turned off, some sort of unrecoverable
error occurs, or a program instruction that halts the computer is encountered.

## Slide 16: Action Categories
Processor-memory
Data transferred from processor to memory or from memory to processor
Processor-I/O
Data transferred to or from a peripheral device by transferring between the processor and an I/O module
Data processing
The processor may perform some arithmetic or logic operation on data
Control
An instruction may specify that the sequence of execution be altered
Notes: In general, these actions fall into four categories:
Processor-memory: Data may be transferred from processor to memory or
from memory to processor.
• Processor-I/O: Data may be transferred to or from a peripheral device by
transferring between the processor and an I/O module.
• Data processing: The processor may perform some arithmetic or logic operation
on data.
• Control: An instruction may specify that the sequence of execution be altered.
For example, the processor may fetch an instruction from location 149, which
specifies that the next instruction be from location 182. The processor will
remember this fact by setting the program counter to 182. Thus, on the next
fetch cycle, the instruction will be fetched from location 182 rather than 150.
An instruction’s execution may involve a combination of these actions.

## Slide 17
Notes: Consider a simple example using a hypothetical machine that includes the
characteristics listed in Figure 3.4. The processor contains a single data register,
called an accumulator (AC). Both instructions and data are 16 bits long. Thus, it is
convenient to organize memory using 16-bit words. The instruction format provides
4 bits for the opcode, so that there can be as many as 24 = 16 different opcodes, and
up to 212 = 4096 (4K) words of memory can be directly addressed.

## Slide 18
Notes: Figure 3.5 illustrates a partial program execution, showing the relevant
portions of memory and processor registers. The program fragment shown adds
the contents of the memory word at address 940 to the contents of the memory
word at address 941 and stores the result in the latter location. Three instructions,
which can be described as three fetch and three execute cycles, are required:
1. The PC contains 300, the address of the first instruction. This instruction (the
value 1940 in hexadecimal) is loaded into the instruction register IR, and
the PC is incremented. Note that this process involves the use of a memory
address register and a memory buffer register. For simplicity, these intermediate
registers are ignored.
2. The first 4 bits (first hexadecimal digit) in the IR indicate that the AC is to be
loaded. The remaining 12 bits (three hexadecimal digits) specify the address
(940) from which data are to be loaded.
3. The next instruction (5941) is fetched from location 301, and the PC is
incremented.
4. The old contents of the AC and the contents of location 941 are added, and
the result is stored in the AC.
5. The next instruction (2941) is fetched from location 302, and the PC is
incremented.
6. The contents of the AC are stored in location 941.
In this example, three instruction cycles, each consisting of a fetch cycle and an
execute cycle, are needed to add the contents of location 940 to the contents of 941.
With a more complex set of instructions, fewer cycles would be needed. Some older
processors, for example, included instructions that contain more than one memory
address. Thus, the execution cycle for a particular instruction on such processors could
involve more than one reference to memory. Also, instead of memory references, an
instruction may specify an I/O operation.

## Slide 19
Example Program Execution
The PC contains 300, the address of the first instruction.
  Value at address 300 is loaded (1940) into IR
  First digit (1) is the op code (Load AC)
  The last three digits are the address (940)
First instruction is implemented (0003 loaded to AC) and PC is incremented
Next instruction (address 301) is loaded (5941) into IR
  First digit (5) is the op code (Add to AC)
  The last three are the address (941)
The data at address 941 are added to the AC and the PC is incremented
Next instruction (address 302) is loaded (2941) into IR
  First digit (2) is the op code (Store AC)
  The last three are the address (941)
The contents of the AC are written to memory and the PC is incremented

## Slide 21
Notes: The execution cycle for a particular instruction may involve more than one
reference to memory. Also, instead of memory references, an instruction may specify
an I/O operation. With these additional considerations in mind, Figure 3.6 provides
a more detailed look at the basic instruction cycle of Figure 3.3. The figure is in the
form of a state diagram.
For any given instruction cycle, some states may be null and
others may be visited more than once. The states can be described as follows:
• Instruction address calculation (iac): Determine the address of the next
instruction to be executed. Usually, this involves adding a fixed number to
the address of the previous instruction. For example, if each instruction is 16
bits long and memory is organized into 16-bit words, then add 1 to the previous
address. If, instead, memory is organized as individually addressable 8-bit
bytes, then add 2 to the previous address.
• Instruction fetch (if): Read instruction from its memory location into the
processor.
• Instruction operation decoding (iod): Analyze instruction to determine type
of operation to be performed and operand(s) to be used.
• Operand address calculation (oac): If the operation involves reference to an
operand in memory or available via I/O, then determine the address of the
operand.
• Operand fetch (of): Fetch the operand from memory or read it in from I/O.
• Data operation (do): Perform the operation indicated in the instruction.
• Operand store (os): Write the result into memory or out to I/O.
States in the upper part of Figure 3.6 involve an exchange between the
processor and either memory or an I/O module. States in the lower part of the
diagram involve only internal processor operations. The oac state appears twice,
because an instruction may involve a read, a write, or both. However, the action performed
during that state is fundamentally the same in both cases, and so only a single
state identifier is needed.
Also note that the diagram allows for multiple operands and multiple results,
because some instructions on some machines require this. For example, the PDP-11
instruction ADD A,B results in the following sequence of states: iac, if, iod, oac, of,
oac, of, do, oac, os.
Finally, on some machines, a single instruction can specify an operation to be performed
on a vector (one-dimensional array) of numbers or a string (one-dimensional
array) of characters. As Figure 3.6 indicates, this would involve repetitive operand fetch
and/or store operations.

## Slide 22: Instruction cycle statements
Instruction fetch (if): Read instruction from its memory location into the
processor.
Instruction operation decoding (iod): Analyze instruction to determine type
of operation to be performed and operand(s) to be used.
Operand address calculation (oac): If the operation involves reference to an
operand in memory or available via I/O, then determine the address of the
operand.
Operand fetch (of): Fetch the operand from memory or read it in from I/O.
Data operation (do): Perform the operation indicated in the instruction.
Operand store (os): Write the result into memory or out to I/O.

## Slide 23
Interrupts
An interrupt allows some module (I/O, memory) to stop the normal processing of the processor
  It may or may not resume processing after handling the interrupt
Interrupts are a way to improve processing efficiency
  External devices are slower than the processor
  We don’t want the processor to wait for the printer
  The printer can interrupt the processor when it needs attention
Interrupts are also used to stop a process when some type of error has occurred
  The error may or may not be recoverable

## Slide 24
Table 3.1
Classes of Interrupts
Notes: Virtually all computers provide a mechanism by which other modules (I/O, memory)
may interrupt the normal processing of the processor. Table 3.1 lists the most common
classes of interrupts. The specific nature of these interrupts is examined
later in this book, especially in Chapters 7 and 14. However, we need to introduce the concept
now to understand more clearly the nature of the instruction cycle and the implications
of interrupts on the interconnection structure.

## Slide 25
Notes: From the point of view of the user program, an interrupt is just that: an interruption
of the normal sequence of execution. When the interrupt processing is completed,
execution resumes (Figure 3.8). Thus, the user program does not have to contain any
special code to accommodate interrupts; the processor and the operating system are
responsible for suspending the user program and then resuming it at the same point.

## Slide 26
Notes: Interrupts are provided primarily as a way to improve processing efficiency.
For example, most external devices are much slower than the processor. Suppose
that the processor is transferring data to a printer using the instruction cycle scheme
of Figure 3.3. After each write operation, the processor must pause and remain
idle until the printer catches up. The length of this pause may be on the order of
many hundreds or even thousands of instruction cycles that do not involve memory.
Clearly, this is a very wasteful use of the processor.
Figure 3.7a illustrates this state of affairs. The user program performs a series
of WRITE calls interleaved with processing. Code segments 1, 2, and 3 refer to
sequences of instructions that do not involve I/O. The WRITE calls are to an I/O
program that is a system utility and that will perform the actual I/O operation. The
I/O program consists of three sections:
• A sequence of instructions, labeled 4 in the figure, to prepare for the actual
I/O operation. This may include copying the data to be output into a special
buffer and preparing the parameters for a device command.
• The actual I/O command. Without the use of interrupts, once this command is
issued, the program must wait for the I/O device to perform the requested function
(or periodically poll the device). The program might wait by simply repeatedly
performing a test operation to determine if the I/O operation is done.
• A sequence of instructions, labeled 5 in the figure, to complete the operation.
This may include setting a flag indicating the success or failure of the operation.
Because the I/O operation may take a relatively long time to complete, the I/O
program is hung up waiting for the operation to complete; hence, the user program
is stopped at the point of the WRITE call for some considerable period of time.
With interrupts, the processor can
be engaged in executing other instructions while an I/O operation is in progress.
Consider the flow of control in Figure 3.7b. As before, the user program reaches a
point at which it makes a system call in the form of a WRITE call. The I/O program
that is invoked in this case consists only of the preparation code and the actual I/O
command. After these few instructions have been executed, control returns to the
user program. Meanwhile, the external device is busy accepting data from computer
memory and printing it. This I/O operation is conducted concurrently with the
execution of instructions in the user program.
When the external device becomes ready to be serviced—that is, when it is
ready to accept more data from the processor—the I/O module for that external
device sends an interrupt request signal to the processor. The processor responds by
suspending operation of the current program, branching off to a program to service
that particular I/O device, known as an interrupt handler, and resuming the original
execution after the device is serviced. The points at which such interrupts occur are
indicated by an asterisk in Figure 3.7b.
Let us try to clarify what is happening in Figure 3.7. We have a user program
that contains two WRITE commands. There is a segment of code at the beginning,
then one WRITE command, then a second segment of code, then a second WRITE
command, then a third and final segment of code. The WRITE command invokes the
I/O program provided by the OS. Similarly, the I/O program consists of a segment
of code, followed by an I/O command, followed by another segment of code. The I/O
command invokes a hardware I/O operation.

## Slide 27
Interrupts
In these examples a “write” involves three steps:
  Preprocessing
  The write itself which takes place on a peripheral device
  Post processing
The first system, without interrupts, must wait during each write operation
The second system, with interrupts, can initiate the write and then proceed with normal operations
  When the write is complete the processor is interrupted do the postprocessing necessary at the end of the write
On the third system the processor tries to initiate a second write before the first is completed
  Again, even with interrupts, the processor must wait

## Slide 28
Priority Interrupts
As an example of this second approach, consider a system with three I/O devices: a printer, a disk, and a communications line, with increasing priorities of 2, 4, and 5, respectively
  A user program begins at t = 0
  At t = 10, a printer interrupt occurs
  While printer interrupt service routine (ISR) is still executing, at t = 15, a communications interrupt occurs.
    Because the communications line has higher priority than the printer, the interrupt is honored. The printer ISR is interrupted
  While this routine is executing, a disk interrupt occurs (t = 20)
    Because this interrupt is of lower priority, it is simply held, and the communications ISR runs to completion.
  When the communications ISR is complete (t = 25), the system processes the disk ISR because it has a higher priority
  Only when that routine is complete (t = 35) is the printer ISR resumed.
  When that routine completes (t = 40), control finally returns to the user program.

## Slide 29: I/O Function
In addition to exchanging data with memory, the processor can exchange data directly with I/O modules
I/O modules control one or more devices
Processor can read data from or write data to an I/O module
Processor identifies a specific device that is controlled by a particular I/O module
I/O instructions rather than memory referencing instructions
In some cases it is desirable to allow I/O exchanges to occur directly with memory
The processor grants to an I/O module the authority to read from or write to memory so that the I/O memory transfer can occur without tying up the processor
The I/O module issues read or write commands to memory relieving the processor of responsibility for the exchange
This operation is known as direct memory access (DMA)
Notes: An I/O module (e.g., a disk controller) can exchange data directly with the
processor. Just as the processor can initiate a read or write with memory, designating
the address of a specific location, the processor can also read data from or write data
to an I/O module. In this latter case, the processor identifies a specific device that is
controlled by a particular I/O module. Thus, an instruction sequence similar in form to
that of Figure 3.5 could occur, with I/O instructions rather than memory-referencing
instructions.
In some cases, it is desirable to allow I/O exchanges to occur directly with
memory. In such a case, the processor grants to an I/O module the authority to read
from or write to memory, so that the I/O-memory transfer can occur without tying up
the processor. During such a transfer, the I/O module issues read or write commands
to memory, relieving the processor of responsibility for the exchange. This operation
is known as direct memory access (DMA) and is examined in Chapter 7.

## Slide 30: The interconnection structure must support the following types of transfers:
Memory to processor
Processor reads an instruction or a unit of data from memory
Processor to memory
Processor writes a unit of data to memory
I/O to processor
Processor reads data from an I/O device via an I/O module
Processor to I/O
Processor sends data to the I/O device
I/O to or from memory
An I/O module is allowed to exchange data directly with memory without going through the processor using direct memory access
Notes: The preceding list defines the data to be exchanged. The interconnection
structure must support the following types of transfers:
• Memory to processor: The processor reads an instruction or a unit of data
from memory.
• Processor to memory: The processor writes a unit of data to memory.
• I/O to processor: The processor reads data from an I/O device via an I/O
module.
• Processor to I/O: The processor sends data to the I/O device.
• I/O to or from memory: For these two cases, an I/O module is allowed to exchange
data directly with memory, without going through the processor, using
direct memory access.
Over the years, a number of interconnection structures have been tried. By
far the most common are (1) the bus and various multiple-bus structures, and (2)
point-to-point interconnection structures with packetized data transfer. We devote
the remainder of this chapter for a discussion of these structures.

## Slide 31: Bus Interconnection
There needs to be a means for the different components of a computer system to communicate
Modern general-purpose computers use various specialized point-to-point interconnection structures
A common bus structure was previously dominant and is still used for many embedded systems
  Multiple devices connect to the bus
  A signal transmitted by one device can be received by any device on the bus
  The devices must be synchronized so that signals do not overlap
Notes: An I/O module (e.g., a disk controller) can exchange data directly with the
processor. Just as the processor can initiate a read or write with memory, designating
the address of a specific location, the processor can also read data from or write data
to an I/O module. In this latter case, the processor identifies a specific device that is
controlled by a particular I/O module. Thus, an instruction sequence similar in form to
that of Figure 3.5 could occur, with I/O instructions rather than memory-referencing
instructions.
In some cases, it is desirable to allow I/O exchanges to occur directly with
memory. In such a case, the processor grants to an I/O module the authority to read
from or write to memory, so that the I/O-memory transfer can occur without tying up
the processor. During such a transfer, the I/O module issues read or write commands
to memory, relieving the processor of responsibility for the exchange. This operation
is known as direct memory access (DMA) and is examined in Chapter 7.

## Slide 32: Bus Interconnection
A communication pathway connecting two or more devices
Key characteristic is that it is a shared transmission medium
Signals transmitted by any one device are available for reception by all other devices attached to the bus
If two devices transmit during the same time period their signals will overlap and become garbled
Typically consists of multiple communication lines
Each line is capable of transmitting signals representing binary 1 and binary 0
Computer systems contain a number of different buses that provide pathways between components at various levels of the computer system hierarchy
System bus
A bus that connects major computer components (processor, memory, I/O)
The most common computer interconnection structures are based on the use of one or more system buses
Notes: The bus was the dominant means of computer system component interconnection
for decades. For general-purpose computers, it has gradually given way to various
point-to-point interconnection structures, which now dominate computer system
design. However, bus structures are still commonly used for embedded systems, particularly
microcontrollers. In this section, we give a brief overview of bus structure.
Appendix C provides more detail.
A bus is a communication pathway connecting two or more devices. A key characteristic
of a bus is that it is a shared transmission medium. Multiple devices connect
to the bus, and a signal transmitted by any one device is available for reception by
all other devices attached to the bus. If two devices transmit during the same time
period, their signals will overlap and become garbled. Thus, only one device at a
time can successfully transmit.
Typically, a bus consists of multiple communication pathways, or lines. Each
line is capable of transmitting signals representing binary 1 and binary 0. Over time,
a sequence of binary digits can be transmitted across a single line. Taken together,
several lines of a bus can be used to transmit binary digits simultaneously (in parallel).
For example, an 8-bit unit of data can be transmitted over eight bus lines.
Computer systems contain a number of different buses that provide pathways
between components at various levels of the computer system hierarchy. A bus that
connects major computer components (processor, memory, I/O) is called a system
bus. The most common computer interconnection structures are based on the use of
one or more system buses.

## Slide 33: Data Bus
Data lines that provide a path for moving data among system modules
May consist of 32, 64, 128, or more separate lines
The number of lines is referred to as the width of the data bus
The number of lines determines how many bits can be transferred at a time
The width of the data bus is a key factor in determining overall
system performance
Notes: A system bus consists, typically, of from about fifty to hundreds of separate lines.
The data lines provide a path for moving data among system modules. These
lines, collectively, are called the data bus. The data bus may consist of 32, 64, 128, or
even more separate lines, the number of lines being referred to as the width of the
data bus. Because each line can carry only 1 bit at a time, the number of lines determines
how many bits can be transferred at a time. The width of the data bus is a key
factor in determining overall system performance. For example, if the data bus is
32 bits wide and each instruction is 64 bits long, then the processor must access the
memory module twice during each instruction cycle.

## Slide 34: Address Bus Control Bus
Used to designate the source or destination of the data on the data bus
  If the processor wishes to read a word of data from memory it puts the address of the desired word on the address lines
Width determines the maximum possible memory capacity of the system
Also used to address I/O ports
  The higher order bits are used to select a particular module on the bus and the lower order bits select a memory location or I/O port within the module
Used to control the access and the use of the data and address lines
Because the data and address lines are shared by all components there must be a means of controlling their use
Control signals transmit both command and timing information among system modules
Timing signals indicate the validity of data and address information
Command signals specify operations to be performed
Notes: The address lines are used to designate the source or destination of the data on
the data bus. For example, if the processor wishes to read a word (8, 16, or 32 bits)
of data from memory, it puts the address of the desired word on the address lines.
Clearly, the width of the address bus determines the maximum possible memory
capacity of the system. Furthermore, the address lines are generally also used to
address I/O ports. Typically, the higher-order bits are used to select a particular
module on the bus, and the lower-order bits select a memory location or I/O port
within the module. For example, on an 8-bit address bus, address 01111111 and
below might reference locations in a memory module (module 0) with 128 words
of memory, and address 10000000 and above refer to devices attached to an I/O
module (module 1).
The control lines are used to control the access to and the use of the data and
address lines. Because the data and address lines are shared by all components,
there must be a means of controlling their use. Control signals transmit both command
and timing information among system modules. Timing signals indicate the
validity of data and address information. Command signals specify operations to be
performed. Typical control lines include:
• Memory write: causes data on the bus to be written into the addressed location
• Memory read: causes data from the addressed location to be placed on the
bus
• I/O write: causes data on the bus to be output to the addressed I/O port
• I/O read: causes data from the addressed I/O port to be placed on the bus
• Transfer ACK: indicates that data have been accepted from or placed on the
bus
• Bus request: indicates that a module needs to gain control of the bus
• Bus grant: indicates that a requesting module has been granted control of the
bus
• Interrupt request: indicates that an interrupt is pending
• Interrupt ACK: acknowledges that the pending interrupt has been recognized
• Clock: is used to synchronize operations
• Reset: initializes all modules

## Slide 35
Notes: Each line is assigned a particular meaning or function. Although there are
many different bus designs, on any bus the lines can be classified into three functional
groups (Figure 3.16): data, address, and control lines. In addition, there may
be power distribution lines that supply power to the attached modules.
The operation of the bus is as follows. If one module wishes to send data to
another, it must do two things: (1) obtain the use of the bus, and (2) transfer data
via the bus. If one module wishes to request data from another module, it must (1)
obtain the use of the bus, and (2) transfer a request to the other module over the
appropriate control and address lines. It must then wait for that second module to
send the data.

## Slide 36: Point-to-Point Interconnect
Principal reason for change was the electrical constraints encountered with increasing the frequency of wide synchronous buses
At higher and higher data rates it becomes increasingly difficult to perform the synchronization and arbitration functions in a timely fashion
A conventional shared bus on the same chip magnified the difficulties of increasing bus data rate and reducing bus latency to keep up with the processors
Has lower latency, higher data rate, and better scalability
Notes: The shared bus architecture was the standard approach to interconnection between
the processor and other components (memory, I/O, and so on) for decades. But
contemporary systems increasingly rely on point-to-point interconnection rather
than shared buses.
The principal reason driving the change from bus to point-to-point interconnect
was the electrical constraints encountered with increasing the frequency of wide
synchronous buses. At higher and higher data rates, it becomes increasingly difficult
to perform the synchronization and arbitration functions in a timely fashion. Further,
with the advent of multi-core chips, with multiple processors and significant memory
on a single chip, it was found that the use of a conventional shared bus on the same
chip magnified the difficulties of increasing bus data rate and reducing bus latency
to keep up interconnect has lower latency, higher data rate, and better scalability.

## Slide 37: Quick Path Interconnect
Introduced in 2008
Multiple direct connections
    Direct pairwise connections to other components eliminating the need for arbitration found in shared transmission systems
Layered protocol architecture
    These processor level interconnects use a layered protocol architecture rather than the simple use of control signals found in shared bus arrangements
Packetized data transfer
    Data are sent as a sequence of packets each of which includes control headers and error control codes
QPI
Notes: In this section, we look at an important and representative example of the
point-to-point interconnect approach: Intel’s QuickPath Interconnect (QPI), which
was introduced in 2008.
The following are significant characteristics of QPI and other point-to-point
interconnect schemes:
• Multiple direct connections: Multiple components within the system enjoy
direct pairwise connections to other components. This eliminates the need for
arbitration found in shared transmission systems.
• Layered protocol architecture: As found in network environments, such as
TCP/IP-based data networks, these processor-level interconnects use a layered
protocol architecture, rather than the simple use of control signals found in
shared bus arrangements.
• Packetized data transfer: Data are not sent as a raw bit stream. Rather, data
are sent as a sequence of packets, each of which includes control headers and
error control codes.

## Slide 38
Notes: Figure 3.17 illustrates a typical use of QPI on a multi-core computer. The
QPI links (indicated by the green arrow pairs in the figure) form a switching fabric
that enables data to move throughout the network. Direct QPI connections can be
established between each pair of core processors. If core A in Figure 3.20 needs to
access the memory controller in core D, it sends its request through either cores B
or C, which must in turn forward that request on to the memory controller in core D.
Similarly, larger systems with eight or more processors can be built using processors
with three links and routing traffic through intermediate processors.
In addition, QPI is used to connect to an I/O module, called an I/O hub (IOH).
The IOH acts as a switch directing traffic to and from I/O devices. Typically in newer
systems, the link from the IOH to the I/O device controller uses an interconnect
technology called PCI Express (PCIe), described later in this chapter. The IOH translates
between the QPI protocols and formats and the PCIe protocols and formats. A
core also links to a main memory module (typically the memory uses dynamic access
random memory (DRAM) technology) using a dedicated memory bus.

## Slide 39: QPI Layers
QPI is defined as a four-layer protocol architecture:
Physical Layer: the actual wires carrying signals, along with the circuitry and logic to support the transfer of 1’s and 0’s.
  The unit of data transfer at the physical layer is 20 bits, which is called a Phit (physical unit)
Link Layer: responsible for reliable transmission and flow control.
  The link layer’s unit of transfer is an 80 bit Flit (flow control unit)
Routing Layer: Provides the framework for directing packets.
Protocol Layer: The high-level set of rules for exchanging packets of data between devices. A packet is an integral number of Flits.
Notes: A system bus consists, typically, of from about fifty to hundreds of separate lines.
The data lines provide a path for moving data among system modules. These
lines, collectively, are called the data bus. The data bus may consist of 32, 64, 128, or
even more separate lines, the number of lines being referred to as the width of the
data bus. Because each line can carry only 1 bit at a time, the number of lines determines
how many bits can be transferred at a time. The width of the data bus is a key
factor in determining overall system performance. For example, if the data bus is
32 bits wide and each instruction is 64 bits long, then the processor must access the
memory module twice during each instruction cycle.

## Slide 40
Notes: QPI is defined as a four-layer protocol architecture, encompassing the
following layers (Figure 3.18):
• Physical: Consists of the actual wires carrying the signals, as well as circuitry
and logic to support ancillary features required in the transmission and receipt
of the 1s and 0s. The unit of transfer at the Physical layer is 20 bits, which is
called a Phit (physical unit).
Link: Responsible for reliable transmission and flow control. The Link layer’s
unit of transfer is an 80-bit Flit (flow control unit).
• Routing: Provides the framework for directing packets through the fabric.
• Protocol: The high-level set of rules for exchanging packets of data between
devices. A packet is comprised of an integral number of Flits.

## Slide 41: QPI Physical Layer
The previous figure shows the physical architecture of a QPI port
The QPI port consists of 84 individual links grouped as follows
Each data path consists of a pair of wires that transmits data one bit at a time; each pair is referred to as a lane
There are 20 data lanes in each direction (transmit and receive), plus a clock lane in each direction
Thus, QPI is capable of transmitting 20 bits in parallel in each direction
Notes: A system bus consists, typically, of from about fifty to hundreds of separate lines.
The data lines provide a path for moving data among system modules. These
lines, collectively, are called the data bus. The data bus may consist of 32, 64, 128, or
even more separate lines, the number of lines being referred to as the width of the
data bus. Because each line can carry only 1 bit at a time, the number of lines determines
how many bits can be transferred at a time. The width of the data bus is a key
factor in determining overall system performance. For example, if the data bus is
32 bits wide and each instruction is 64 bits long, then the processor must access the
memory module twice during each instruction cycle.

## Slide 42: Peripheral Component Interconnect (PCI)
A popular high bandwidth, processor independent bus that can function as a mezzanine or peripheral bus
Delivers better system performance for high speed I/O subsystems
PCI Special Interest Group (SIG)
  Created to develop further and maintain the compatibility of the PCI specifications
  PCI Express (PCIe)
  Point-to-point interconnect scheme intended to replace bus-based schemes such as PCI
  Key requirement is high capacity to support the needs of higher data rate I/O devices, such as Gigabit Ethernet
  Another requirement deals with the need to support time dependent data streams
Notes: The peripheral component interconnect (PCI) is a popular high-bandwidth, processor independent
bus that can function as a mezzanine or peripheral bus. Compared with
other common bus specifications, PCI delivers better system performance for high speed
I/O subsystems (e.g., graphic display adapters, network interface controllers,
and disk controllers).
Intel began work on PCI in 1990 for its Pentium-based systems. Intel soon
released all the patents to the public domain and promoted the creation of an
industry association, the PCI Special Interest Group (SIG), to develop further and
maintain the compatibility of the PCI specifications. The result is that PCI has been
widely adopted and is finding increasing use in personal computer, workstation, and
server systems. Because the specification is in the public domain and is supported
by a broad cross section of the microprocessor and peripheral industry, PCI products
built by different vendors are compatible.
As with the system bus discussed in the preceding sections, the bus-based PCI
scheme has not been able to keep pace with the data rate demands of attached
devices. Accordingly, a new version, known as PCI Express (PCIe) has been developed.
PCIe, as with QPI, is a point-to-point interconnect scheme intended to replace
bus-based schemes such as PCI.
A key requirement for PCIe is high capacity to support the needs of higher data
rate I/O devices, such as Gigabit Ethernet. Another requirement deals with the need
to support time-dependent data streams. Applications such as video-on-demand and
audio redistribution are putting real-time constraints on servers too. Many communications
applications and embedded PC control systems also process data in real-
time.
Today’s platforms must also deal with multiple concurrent transfers at ever-increasing
data rates. It is no longer acceptable to treat all data as equal—it is more important,
for example, to process streaming data first since late real-time data is as useless as no
data. Data needs to be tagged so that an I/O system can prioritize its flow throughout
the platform.

## Slide 43
Notes: Figure 3.21 shows a typical configuration that supports the use of PCIe. A root
complex device, also referred to as a chipset or a host bridge, connects the processor
and memory subsystem to the PCI Express switch fabric comprising one or
more PCIe and PCIe switch devices. The root complex acts as a buffering device, to
deal with difference in data rates between I/O controllers and memory and processor
components. The root complex also translates between PCIe transaction formats
and the processor and memory signal and control requirements. The chipset
will typically support multiple PCIe ports, some of which attach directly to a PCIe
device and one or more that attach to a switch that manages multiple PCIe streams.
PCIe links from the chipset may attach to the following kinds of devices that implement
PCIe:
• Switch: The switch manages multiple PCIe streams.
• PCIe endpoint: An I/O device or controller that implements PCIe, such as
a Gigabit Ethernet switch, a graphics or video controller, disk interface, or a
communications controller.
• Legacy endpoint: Legacy endpoint category is intended for existing designs
that have been migrated to PCI Express, and it allows legacy behaviors such
as use of I/O space and locked transactions. PCI Express endpoints are not
permitted to require the use of I/O space at runtime and must not use locked
transactions. By distinguishing these categories, it is possible for a system
designer to restrict or eliminate legacy behaviors that have negative impacts
on system performance and robustness.
• PCIe/PCI bridge: Allows older PCI devices to be connected to PCIe-based
systems.

## Slide 44: Assignment
Chapter 3
Review Questions:
3.2, 3.3, 3.5
A Top-Level View of Computer Function and Interconnection
  Problems:
  3.1, 3.3, 3.5, 3.11, 3.12, 3.14
Notes: Chapter 3 homework.