## Slide 7
Setup time is the amount of time required for the input to a Flip-Flop to be stable before a clock edge

## Slide 8
Hold time is similar to setup time, but it deals with events after a clock edge occurs. Hold time is the minimum amount of time required for the input to a Flip-Flop to be stable after a clock edge

## Slide 10
If your design has setup or hold time violations, the Flip-Flop output is not guaranteed to be stable. It could be zero, it could be one, it could be somewhere in the middle, it’s not known. This is called metastability

## Slide 11
If your design has setup or hold time violations, the Flip-Flop output is not guaranteed to be stable. It could be zero, it could be one, it could be somewhere in the middle, it’s not known. This is called metastability

## Slide 12
Propagation delay is the amount of time required for a signal to be received after it has been sent; it is caused by the time it takes for the signal to travel through a medium. Propagation delay is of primary interest in electronic circuit design and computer networking, although all signals will inherently experience some form of propagation delay.