## Slide 1: RAM AND ROM TYPES

## Slide 2: Types of ram
1.Dynamic RAM: Its also called (DRAM) is the most common kind of random access memory (RAM) used in desktop and laptop computers.
It looks like chip can be connected to slot at mother board.
DRAM stores its information in a cell containing a capacitor and transistor.
What is a capacitor? It store electrical energy.
What is a transistor? transistor used to control the amount of current or voltage or used for amplification or switching of an electronic signal (short for transfer resistance) .
1 capacitor and transistor store one bit of data. either 1 or 0.
Inside a 1 ram chip there are millions of small capacitors & transistors

## Slide 3: Continue……………
In DRAM Refreshing is required in every few milliseconds.
This refreshing is done by the memory controller located on the chipset of the motherboard
because of this design, these cells must be refreshed with new electricity every few milliseconds
Allowing the memory to keep its charge and hold the data as long as needed.
DRAM was first invented and by Robert Dennard in 1968 and first released commercially by Intel in October 1970
10-1Deci
10-2Centi
10-3Milli
10-6Micro
10-9Nano
10-12Pico

## Slide 4: 2.Static RAM-sram
It stands for Static Random Access Memory.
Its embedded with mother board.
SRAM is more expensive, faster, and more power-efficient than DRAM.
No refreshing required in SRAM.
SRAM uses flip flops & transistors for storing data.
Flip flop: is a circuit or device used to store information.
SRAM use as a cache memory in computer

## Slide 5: Cache memory
Cache memory: it is a random access memory (RAM) that a computer microprocessor can access more quickly than it can access regular RAM.
The cache is a smaller, faster memory which stores copies of the data which is frequently in use.
When the processor needs to read from or write to a location in main memory, it first checks whether a copy of that data is in the cache. If so, the processor immediately reads from or writes to the cache, which is much faster than reading from or writing to main memory.
It boost system performance.

## Slide 6: Types of cache memory
L1-LEVEL 1 CACHE:
L1 is "level-1" cache memory, usually built onto the microprocessor.
It is small in size than L2.
It is more faster than L2.
In L1 frequently used instructions are stored.
Processor first looks into L1 for access data.
L2-LEVEL 2 CACHE:
L2 is "level-2" cache memory, usually built onto the motherboard.
It is large in size than L1.
It is slower than L1 but faster than main memory.
In L2 predicable instructions are stored.

## Slide 7: Types of rom
1- PROM(Programmable Read Only Memory) This form of ROM is initially blank.
The programmer can write data/program on it by using special devices.
However, once the program or data is written in PROM chip, it cannot be changed.
If there is an error occurs in writing instructions or data in PROM, the error cannot be erased.
In the result PROM chip becomes unusable.
The key difference from a standard ROM is that the data is written into a ROM during manufacture, while with a PROM the data is programmed into them after manufacture.
PROMs are used in digital electronic devices to store permanent data such as video game consoles mobile phones and medical devices.

## Slide 8: Continue………
EPROM ---Erasable Programmable Read Only Memory.
This form of ROM is also initially blank
The program or data can be written by programmer or manufacture by using special devices and ultraviolet rays.
In EPROM chip modification in data is possible.
Data can be erase or add.
The main difference between EPROM chips and Programmable Read-Only Memory (PROM) chips is that the EPROM chips can be programmed more than one time, while PROM chips are not re-programmable.
EPROMs are used not only in computers.

## Slide 9: Continue………
3- EEPROM Electrically Erasable Programmable Read Only Memory.
EEPROM was a replacement for PROM and EPROM chips
This kind of ROM can be written or changed with the help of electrical devices.
So data stored in this type of ROM chip can be easily modified.
EEPROM memory is used in computers as well as other electronic devices in order to store small amounts of data.